## Slide 1
Context Sensitive Systems – Introduction to Context Recognition

## Slide 2: Content of this lecture
Context and Motivation
Sensors and Middleware
/ 8. Features in Data
/ 9. Prediction
/ 10. Classification
Vertical Application
Fusing Knowledge
Context oriented Programming

## Slide 3: Definition transducer
A transducer is a device that converts one form of energy to another form of energy. Energy types include/(but are not limited to) electrical, mechanical, electromagnetic (including light), chemical, acoustic, and thermal energy. (for example, a loudspeaker converts an electric signal to sound),
A sensor is a transducer whose purpose is to sense (that is, to detect) some characteristic of its environs. A sensor is used to detect a parameter in one form and report it in another form of energy, often an electrical signal.

## Slide 4: Sensor and Context
Sensor
Beacon/ Reflector
External Energy Source
Context c with hidden state
Context c transforms signal s to s’ at state x c(,s)=s’
Context Recognition is learning c’-1 so that c’-1(s,s’)=
Typical is only nominal and c is no function and c-1 does not exist, so why even try to model it???

## Slide 5: Unconventional Sensors
Undertanding the sensor becomes important!
Notes: This context awareness and novel form of HCI is based on sensors.
What we used in the Retail Store Application are special types of sensors as the one you see here, that is a extreme high sensitive movement sensor system with almost 0 energy consumption that we develop togehter with Prof. Weber from the IPE (Institut für Prozessdatenverarbeitung und Elektronik) from the Helmholtz Part.
Now we have sensors and we want to build context aware systems out of it. How do we do this?

## Slide 6: Detection Chain
Feature Extraction & Reduction
Physical Pheno-menon
Activity
Detection
Normalization
Classification
Phenomenon
(e.g. Context Value)
Reasoning
Activity
Physical Pheno-menon
Activity
Detection
Classification
Activity
Ubicomp: Assignments correlated / learned
Classical Measurement methods: Each step analytically modelled

## Slide 7: Measurement in the 21st century
„A set of observations that reduce uncertainty where the result is expressed as a quantity” Douglas Hubbard: "How to Measure Anything", Wiley (2007)
Result of a measurement: value, mean, other statistical values e.g. standard deviation
  In this sense, a good guess may not be worse than a bad measurement

## Slide 8: Activity Recognition Using RF Signals

## Slide 9
Middleware

## Slide 10: Communication and Context
Sensor
Sensor
Sensor
Analytics Node
Sensor Node
What is the main role of context in communication?
What type of context is relevant here?

## Slide 11: Interoperability
In order to interoperate, two entities must have some shared agreement on the form and function of their communication (could be seen as pre-shared context)
The agreement defines the interfaces each entity exports, and which are known to the other party
  e.g. a web browser and a web server must agree on a set of common protocols (HTTP) as well as format and semantics of data exchanged (usually HTML, XML)
  Web services and their clients must agree upon known service interfaces and protocols for their invocation
The agreement must be a priori, and built-in to each party
 Cognitive aspects (context recognition) typically can only optimize

## Slide 12: How to connect your sensor
20mA
I²C
SPI
MBUS
…

## Slide 13: List of M2M Protocols (source: Wikipedia)
AS-i – Actuator-sensor interface, a low level 2-wire bus establishing power and communications to basic digital and analog devices
BSAP – Bristol Standard Asynchronous Protocol, developed by Bristol Babcock Inc.
CC-Link Industrial Networks – Supported by the CLPA
CIP (Common Industrial Protocol) – can be treated as application layer common to DeviceNet, CompoNet, ControlNet and EtherNet/IP
Controller Area Network utilised in many network implementations, including CANopen and DeviceNet
ControlNet – an implementation of CIP, originally by Allen-Bradley
DeviceNet – an implementation of CIP, originally by Allen-Bradley
DF-1 - used by Allen-Bradley PLC-5, SLC-500, and MicroLogix class devices
DirectNet – Koyo / Automation Direct[1] proprietary, yet documented PLC interface
EtherCAT
Ethernet Global Data (EGD) – GE Fanuc PLCs (see also SRTP)
EtherNet/IP – IP stands for "Industrial Protocol". An implementation of CIP, originally created by Rockwell Automation
Ethernet Powerlink – an open protocol managed by the Ethernet POWERLINK Standardization Group (EPSG).
FINS, Omron's protocol for communication over several networks, including ethernet.
FOUNDATION fieldbus – H1 & HSE
HART Protocol
HostLink Protocol, Omron's protocol for communication over serial links.
Interbus, Phoenix Contact's protocol for communication over serial links, now part of PROFINET IO
MACRO Fieldbus - "Motion and Control Ring Optical" developed by Delta Tau Data Systems.
MECHATROLINK – open protocol originally developed by Yaskawa, supported by the MMA
MelsecNet, supported by Mitsubishi Electric.
Modbus PEMEX
Modbus Plus
Modbus RTU or ASCII or TCP
OSGP – The Open Smart Grid Protocol, a widely use protocol for smart grid devices built on ISO/IEC 14908.1
OpenADR – Open Automated Demand Response; protocol to manage electricity consuming/controlling devices
Optomux – Serial (RS-422/485) network protocol originally developed by Opto 22 in 1982. The protocol was openly documented[2] and over time used for industrial automation applications.
PieP – An Open Fieldbus Protocol
Profibus – by PROFIBUS International.
PROFINET IO
RAPIEnet – Real-time Automation Protocols for Industrial Ethernet
Honeywell SDS – Smart Distributed System – Originally developed by Honeywell. Currently supported by Holjeron.
SERCOS III, Ethernet-based version of SERCOS real-time interface standard
SERCOS interface, Open Protocol for hard real-time control of motion and I/O
SSCNET, Servo System Controller Network by Mitsubishi Electric for control of motion and I/O
GE SRTP – GE Fanuc PLCs
Sinec H1 – Siemens
SynqNet – Danaher
TTEthernet – TTTech
MPI – Multi Point Interface

## Slide 14: Sensor Connectivity: Wireless Protocols

## Slide 15
Information
&Analytisc
Services
CRM
PLM
SRM
Physical World / Things
SCM
EHM
PLM
ERP
Leg- acy
A2A
People
collaboration
B2B
roles
Devices
embedded analytics
alerts
roles
Smart Items
Middleware & Transcoders
IoT Network
Internet of Things and Services
User Presentation

## Slide 16: Example: Linux Foundation IoTivity

## Slide 17: Example IBM IoT Foundations
IBM bluemix based
MQTT as Communication Middleware

## Slide 18: Common Pattern: Pub Sub
Producer
Consumer
Producer
Consumer
Topic 1
Topic 2
Topic 3
subscribe
publish(topic, msg)
Publish subscribe
system
msg
msg
Notes: Multiple subscribers, decoupling
Some examples : email notification on adding connection etc

## Slide 19
INGEST
PROCESS
VISUALIZE
ANALYZE
STORE
Example: Hadoop Architecture

## Slide 20
Scaling Messaging
Notes: single producer to send 10 million messages, 200 bytes each.
single consumer thread
Flush interval 10K
ActiveMQ – syncOnWrite=false, KahaDB
RabbitMQ – mandatory=true, immediate=false, file persistence
the producer throughput in messages/secondKafka produces at the rate of 50K / second with batch size of 1
400K / second with batch size of 50.
These numbers are orders of magnitude higher than that of ActiveMQ and at least twice better than RabbitMQ.
No producer ACKS
more compact storage format
9 bytes/message overhead in Kafka
144 bytes/message overhead in ActiveMQ
Cost of maintaining heavy index structures
One thread in ActiveMQ spent most of its time accessing a B-Tree to maintain message metadata and state

## Slide 21: The real challenge: non-scalable integration
The Combinatorial Complexity of Ongoing Integration
For interoperability, devices have to be programmed to recognize the specific protocols, standards, data formats, and operations of all expected peer devices
If we want to integrate a new device type into a network, all existing devices must be updated
Because developers program against standards known at development time, they can’t accommodate entirely new devices that don’t resemble existing standards

## Slide 22: The 1990s: “Recombinant Computing” (PARC Object Infrastructure, formerly known as Speakeasy)
A small, fixed set of generic interfaces
  presumed to be known to all parties in an interaction
Mobile code for dynamic extension
  sender downloading code to clients for specific protocols, data types
User in the loop
  Decides which devices/service to associate
  Programmatic interfaces define only syntax, user must decide what makes sense

## Slide 23: The 2000s: Namespaces Mobile Users
Interact with local resources
Data cloud follows the user
Space A
Space B
move
 inject personal data reference into local space
Building Applications for Ubiquitous Computing Environments.
Christopher K. Hess, Manuel Román, and Roy H. Campbell, In International Conference on Pervasive Computing (Pervasive 2002), Zurich, Switzerland, August 26-28, 2002.

## Slide 24: Two big problems of mobility
Physical Mobility
  Devices move around
Logical Mobility
  Functionality moves around
In context-aware systems both can make a difference
  Slightly different understanding of middleware in terms of transparency

## Slide 25: Service oriented Computing: Set of Reusable Components
Connected Device Services
WS-Addressing
SOAP 1.2
HTTP
SOAP over UDP
WS-Discovery
WS-Eventing
WS-Transfer
WS-MEX
Devices Profile for Web Services

## Slide 27: Ontologies to describe sensors and measurements

## Slide 28: and sensor networks
SSN Ontology: Sensor is-a Process is-a System

## Slide 29: CISRO Sensor Ontology

## Slide 30: Interoperability w/ code generation
Networks:
869MHz AwareCon
300/869MHz µPart
2.4Ghz 6lowpan
2.4Hz 802.15.4 Proprietär
SOA:
DPWS
Programming Language:
C, C#, Java
SW Plattforms:
Contiki, ParticleOS, Linux/BSD Sockets
HW Plattform:
Pic18F, AR7
OpenRISC,x86
APIs:
Plain C DOM, WCF 4, WS4D
DPWS Gateway-Architektur for industrial Service
High level of code reuse by aspect oriented code generation using XPAND

## Slide 31: OPC - UA

## Slide 32: Socrades: Enterprise Applications

## Slide 33: Protokolle!
MQTT
REST/JSON HTTP, WebSockets/WebRTC (??)
6LowPAN/COAP (also via BT4)
XMPP
HTTP/2 w/ header compression, QUIC (MTU to small??)
OPC-UA, MTConnect
Markus Jung, Samsung, IoT 2015

## Slide 34: 2010s: Web of Things

## Slide 35: The Semantic Web Dream
“The semantic web is a vision of information that is understandable by computers, so computers can perform more of the tedious work involved in finding, combining, and acting upon information on the web.” – Wikipedia
“I have a dream for the Web [in which computers] become capable of analyzing all the data on the Web – the content, links, and transactions between people and computers.”
– Tim Berners-Lee

## Slide 36: Web of Things Framework

## Slide 37: Classical Pattern Recognition
Data come from a transducer
Feature extraction compresses, filters, transcodes, prepares sensor data
Classification interprets features and assigns a class for them (Knowledge required!)
Further abstraction may be added: high level information, reasoning
Feature
Extraction & Reduction
Classification
...
...
Detection (Transducer)
Further Abstraction
Features
Sensor
Data
Class

## Slide 38: Complexity of Recognizing Contexts 2
Complex contexts can only be sensed indirectly
  Context affects environment in various ways
  Sensors sample specific parameters of the same environment
  Context is present in the sensor signal streams
Problems:
  Sensors only sense partial effects of context
  Sensors are noisy
  Different types of the same context may affect sensor signals in different ways

## Slide 39: Context Recognition using Expert Systems
Create program logic to recognize contexts
  IF location==N. Campus || S. Campus THEN
    context := University;
Advantages:
  often correctly recognizes context using expert knowledge
Problems:
  Designer must have in-depth knowledge of how context classes affect parameters measure by sensors
  Recognition limited by development time
Example: recognize the difference between “walking” and “climbing stairs”
  IF ????? THEN
Solution: allow devices to learn difference!

## Slide 40: Machine Learning for Context Recognition
Devices learn to differentiate between context classes
Idea:
  devices experience different contexts through sensors
  Use this experience to learn the difference between
  (Compare: expert’s experience)
Learning results in executable model:
  Sensor signals as input
  Context as output
  IF [[learned parameters]] THEN
    context := University;
Process AKA: pattern matching, pattern recognition, classification
Disadvantages:
  Labeled sensor data must be collected
    NO SIMPLE TASK!
  Classifier can become complex
  Algorithms require time and resources for learning

## Slide 41: The Learning process
Learning based on:
  sensor data history
  annotated context history: “labels”
Learn to recognize correlated sensor signal patterns and contexts
(supervised learning)
Training is “offline”

## Slide 42: Supervised Machine Learning
Supervised learning
Set of training data:
Feature vectors , and labels
Features calculated at end of each sample window, resulting in vector
Vector is classified by classification algorithm, resulting in context label

## Slide 43: The Classification Process
Trained executable object results from learning process
Black box: analog sensor input, discrete symbolic context as output
Level of abstraction increases, trend from numeric, high-volume data (0x3F, 2°C), to symbolic, low-volume context (“walking”, “busy”)

## Slide 44: Data Processing

## Slide 45: Data Processing Chain
Problem:
  Input: often analog, continuous sensor signals
  Output: symbolic, discrete context class
  How do we get from one to the other?
Sampling sensors yields discrete measurements
  High volume, depending on sampling rate
In theory, sensor data as direct input to classifier
  Greatly increases classifier complexity – too much information!
Solution: extract information of importance

## Slide 46: Step 1 – Sample Windows
Specify period of time to be classified
  Segment data into windows of that time length
Problem: window length greatly affects classification results!
Nyquist–Shannon sampling theorem
  Smallest component frequency B Hz, sample rate > 1/(2B) sufficient
  Here: lowest “relevant” frequency C Hz, smallest effective sample window length 1/(2C)
  Example: footfalls .5Hz, sample window 2s for context walking
  Needed for signal reconstruction  needed for context recognintion?
In practice: empirical evaluated for each application!

## Slide 47: Step 2 - Feature Extraction
Goal: extract “important” information for context differentiation (classification), reducing volume and cardinality of values
What information is important? Context and sensor dependent!
Features in time (e.g. mean) and frequency (Fourier Transformation) domain

## Slide 48: Step 3 - Classification
Selected features appended to a “feature vector”
This is data that classifier sees
Training: feature vectors augmented with label
Classification: feature vector calculated (1 sample window, live data)
Classifier estimates context occurring
classification=>
Ft.1
Ft.1
Ft. n-1
…
Ft. n
Ft.1
Ft.1
Ft. n-1
…
Ft. n
Label
Ft.1
Ft.1
Ft. n-1
…
Ft. n
???
Label

## Slide 49: All together now
Dimensionality Reduction / Increased Abstraction

## Slide 50: FEATURE EXTRACTION

## Slide 51: Types of Features by Context
Location
  GPS, WiFi/BlueTooth fingerprint
Walking speed
  Variance of accelerometer
Group affiliation
  Cross-correlation, Kullback-Leibler divergence
Context at work
  Calendar information
DactyLoc: A minimally geo-referenced WiFi+GSM-fingerprint-based localization method for positioning in urban spaces Kristian Cujia, Martin Wirz, Mikkel Baun Kjærgaard, Daniel Roggen and Gerhard Tröster
Recognition of Crowd Behavior from Mobile Sensors with Pattern Analysis and Graph Clustering Methods Daniel Roggen, Martin Wirz, Dirk Helbing and Gerhard Tröster

## Slide 52: Features by Sensor
Wearable context (activity) recognition
  Time domain: mean, root mean square, energy, magnitude area (AUC), variance, standard deviation, mean absolute deviation, correlation (between sensors)
  Frequency domain: FFT peak(s)
Audio context recognition:
  Time domain: zero crossing rate, amplitude fluctuation, amplitude histogram range distribution.
  Frequency domain: frequency centroid, bandwidth, spectral roll-off point, fluctuation of amplitude-spectra, subband band energy ratio, cepstral coefficients (CEP), FFT range magnitude
Video: out of scope!
Others: social networks, radio signals, Electroencephalography (EEG), Motion capturing (Kinect), etc.
Radio Frequency Sensor: mostly same as audio

## Slide 53: How do I find the right features?
Look in related work for similar applications,
If none available, empiricism and heuristics!!
Brute force approach:
  Try them all out, every combination
Optimized:
  Feature selection algorithms (see later)
Automatic feature selection for context recognition in mobile devices, Könönen, et al.
Feature Selection and Activity Recognition from Wearable Sensors, Susanna Pirttikangas, Kaori Fujinami, Tatsuo Nakajima

## Slide 54: Recognition in Ubiquitous Computing
Low Cost sensing
detect a range of abstract conditions (e.g. human activity, machine condition)
that are related to several physical phenomena
the correlation may not be know from the beginning
Implementation
we opportunistically use sensors that are already there (e.g. your mobile)
or we place simple sensors (nodes) in conveniently reachable places

## Slide 55: What is new in Ubicomp/Pervasive/CPS ?
this means we are not in control of
  precise position (if at all)
  type of sensor
  measurement environment
 indirect sensing may be appropriate: light follows movement
 more care and "intelligence" for recognition required

## Slide 56: Sensor may be substituted: Light follows movement

## Slide 57: Supervised Machine Learning Separation function for a feature space