## Slide 1
Context Sensitive Systems Sensors
SS 2016
teco.kit.edu, pcs.tm.kit.edu
Michael Beigl, Till Riedel

## Slide 2: Recap: Schillit’ classes of context-sensitive applications
Dimension 1: Is the adaption done automatic or manual?
Dimension 2: Does the application adapt information access or perform actions?
Task: Two Examples per Class: 10 min break!
Information access
Command execution
Trigger
Output
Manual /explicit
automatic/implicit

## Slide 3: Content of this lecture
Context and Motivation
Sensors and Middleware
/ 8. Features in Data
/ 9. Prediction
/ 10. Classification
Vertical Application
Fusing Knowledge
Context oriented Programming

## Slide 4
Sensors

## Slide 5: Sensors: Motivation
Human Sensors as a model:
  Quantity:
  Multiple sensors provide the feedback to a human to make him „smart“ (to learn, to have redundant sources for a signal etc.)
Sense | Human Organ | Quanitity | Sensor | Physical
Hearing | Ear | 3* 10^4 | Microphone | Sound
Seing | Eye | 2* 10^8 | Photo detector | Light
Smell | Nose | 10^7 | Gas | Gas
Feeling: Warm Feeling: Cold Feeling: Pressure Feeling: Pain | Skin | 10^4 10^5 5*10^5 3*10^6 | Thermo element Thermo element Piezo | Heat Cold Pressure

## Slide 6: Human Senses
Aristoteles five sense definition
sight, hearing, touch, smell, taste
Additional senses
nociception (pain),
equilibrioception (balance),
proprioception & kinesthesia (joint motion and acceleration),
thermoception (temperature differences)

## Slide 7
Sensors

## Slide 8: Motivation Context through Sensors
Sensor Enable new interactions by providing context
  Tilt sensor Orientation
  Light sensor LCD Brightness
Albrecht Schmidt, Michael Beigl, Hans-Werner Gellersen:
There is more to context than location, 1998

## Slide 9: Sensor Development
Accelleration
Light
Proximity
Touch
Camera
GPS
Rotation
Temperature
Compass
Chart: # of Sensors in mobile phones
| 2000 | 2002 | 2004 | 2007 | 2010
 | 0 | 1 | 2 | 4 | 8
Notes: Das HD2 verfügt über einen GPS-Empfänger, einen Näherungs-, Beschleunigungs- und Lichtsensor + Micro + Kamera + touch= 7, davon 2 komplexe
2002: first commercial camera phone complete with infrastructure was the J-SH04, made by Sharp Corporation, had an integrated CCD sensor, with the Sha-Mail (Picture-Mail in Japanese) infrastructure developed in collaboration with Kahn's LightSurf venture, and marketed from 2001 by J-Phone in Japan today owned by Softbank. The first commercial deployment in North America of camera phones was in 2002.
2007: iPhone 2G: Accl, proximity, micro, kamera, touch = 5

## Slide 10: Sensor Examples
So many types...
  How to classify?

## Slide 11: Sensor classification by measure
Direct Physical Measures (SI)
  length, mass, time, electrical current, temperature, molar amount, luminosity
Derivatives
  angle, velocity, frequency, force, momentun, energy, pressure, load, voltage, tension, power,…

## Slide 12: sensor classification by active principle
Electrical measurement of capacity, inductivity, charge, resistance....
passive: generating voltage
  Converting mechanical, chemical, photonic or thermal energy
  Examples: Hall effect, piezo effect, …
active: needs energy
  „probes“ changes of a non-electrical influence using generated signal
  Change in resistance, inductivity, capacity

## Slide 13: Semi conductors
CMOS sensors
arrays & matrices form video sensors
Sensing context from light:
Reconstructing Images
Intensity
Lightspectrum
Movement
„Codes“: 50Hz/100Hz
 Low energy consumption

## Slide 14: MEMS Principle
MEMS =
Micromechanical System Mechanics directly in silicon
Smart Systems

## Slide 16
3D model of the 3-axis CMOS-MEMS accelerometer
SEM of a fabricated 3-axis SCS accelerometer

## Slide 17: MEMS Examples
  Gyroscopes
  Magnetometer
  Barometer
  Hygrometer
  Ultrasound transducers
MEMS gyroscope
Source: http://www.designnews.com/author.asp?doc_id=256404

## Slide 18
Measurement

## Slide 19: Definition transducer
A transducer is a device that converts one form of energy to another form of energy. Energy types include/(but are not limited to) electrical, mechanical, electromagnetic (including light), chemical, acoustic, and thermal energy. (for example, a loudspeaker converts an electric signal to sound),
A sensor is a transducer whose purpose is to sense (that is, to detect) some characteristic of its environs. A sensor is used to detect a parameter in one form and report it in another form of energy, often an electrical signal.

## Slide 20: Capacitive Sensor
Sensor typically includes RC element
Capacity introduces either damping or frequency change

## Slide 21: Classical Pattern Recognition
Data come from a transducer
Feature extraction compresses, filters, transcodes, prepares sensor data
Classification interprets features and assigns a class for them (Knowledge required!)
Further abstraction may be added: high level information, reasoning
Feature
Extraction & Reduction
Classification
...
...
Detection (Transducer)
Further Abstraction
Features
Sensor
Data
Class

## Slide 22: Analog / Digital
In our case: the input to the feature extraction process should be digital. This means there is an Analog/Digital (A/D) conversion in the end of the chain.
WHY not just sensing digital?

## Slide 23: Analog / Digital
In our case: the input to the feature extraction process should be digital. This means there is an Analog/Digital (A/D) conversion in the end of the chain.
WHY: Because reality is analog.
What is the consequence of the world being analog in terms of measurement accuracy?

## Slide 24: Analog / Digital
In our case: the input to the feature extraction process should be digital. This means there is an Analog/Digital (A/D) conversion in the end of the chain.
WHY: Because reality is analog.
What is the consequence of the world being analog in terms of measurement accuracy?
 Rounding Error, reality is infinite precise

## Slide 25: Measurement
Accuracy: degree of exactness to a measurement standard.
Precision : ability of a measurement to be consistently reproduced.
Reliability: consistency of accurate results over consecutive measurements over time.
Traceability: ongoing validations that the measurement of a final product conforms to the original standard of measurement.
[Fundamentals of Dimensional Metrology, Ted Busch, Wilkie Bros Foundation, Delmar Publishers]

## Slide 26: Accuracy vs. Precission

## Slide 27: Measurement: Possible Errors
Statistical error: an error introduced due to measurement principle or noise that is often Gaussian in nature, with mean at the true measurement value. HOW TO HANDLE?
Systematic error: an error introduced due to de-adjustment of the sensor.

## Slide 28: Measurement: Possible Errors
Statistical error: an error introduced due to measurement principle or noise that is often Gaussian in nature, with mean at the true measurement value. This error can be averaged out by taking multiple measurement of the same physical phenomenon
Systematic error: an error introduced due to de-adjustment of the sensor. This error can not be averaged out. HOW TO HANLDE?

## Slide 29: Measurement: Possible Errors
Statistical error: an error introduced due to measurement principle or noise that is often Gaussian in nature, with mean at the true measurement value. This error can be averaged out by taking multiple measurement of the same physical phenomenon
Systematic error: an error introduced due to de-adjustment of the sensor. This error can not be averaged out, but the system can be (re)calibrated.

## Slide 30: Reasons for measurement errors
Internal: Measurement circuity
  E.g. measurement noise due to thermal movement of atoms or the avalanche effect in semiconductors
  Externally induced noise, e.g. 50 Hz signal overlay
External physical phenomena influencing measurement
Misconception

## Slide 31: Classical Sensor Systems
How do we measure classically?
By precisely controlling the measurement conditions!
For a specific problem we identify the physical phenomenon by:
  Direct measurement
  Controlled placement
  Controlled environment
This is the appropriate way for settings where precision is more important than cost
Notes:     direct measurement: we select appropriate sensors that give direct indication of the physical phenomenom
    controlled placement: we place the sensors at the exact location where we need to measure the physical phenomenon
    Controlled environment: we control the measurement environment so that the measurement can be taken without external influences such as noise

## Slide 32: Measurement
Outcome of a measurement process: a normalized sensor value plus a unit
Normalized: a mutually agreed standard defines units for the values of certain physical phenomena. In Germany: DIN 1313
SI Unit system (Système International d’Unités) defines
  metre (m) :SI unit of length
  second (s) :SI unit of time
  kilogram (kg) :SI unit of mass
  ampere (A) :SI unit of electric current
  degree kelvin (K) :SI unit of thermodynamic temperature
  candela (cd) :SI unit of luminous intensity
  Mole (mol): SI unit of chemical substrate
All other units are derived

## Slide 33: Traditional Measurement Process
DIN 1319
Define Measurement task and measurement unit
Specify ALL measurement conditions exactly (conditions of the measurement object, environment
Select a measurement device
Calibrate a measurement device
Specify the measurement process precisely
Take the measurement(s)
Calculate noise influence, systematic measurement error
Calculate overall measurement result and quantitative error margin

## Slide 34: Measurement
Traditional Measurement works in a closed system approach
For complex detection difficult:
Activity  reasoning concluded phenomenon  classification  feature reduction  feature extraction normalization detection measured physical phenomenon
Requires a lot of knowledge about the measurement process (see slide before) before starting
Simpler in Context recognition: Activity  classification  feature extraction  measurements While classification is just trained
Activity
Measurabel Phenomenon (Sensor on Machine)

## Slide 35: Example of a Recognition Process
Sensor data are often an interpretation of an electrical property (e.g. resistance,) which can be measured by an electrical parameter e.g. voltage
000000111000011111100101010111000111
0
1
Quiet.................loud...........average..........
Voltage
Over time
Feature extraction: Avg over time & threshold
Classification: Assign to a class

## Slide 36: Pattern Recognition in general
Here normalized value seem not to play any role
What do you think, is this the case? And if so, why?
Feature
Extraction & Reduction
Classification
...
...
Detection (Transducer /Sensor)
Further Abstraction
Features
Sensor
Data
Class

## Slide 37: Sensor and Context
Sensor
Beacon/ Reflector
External Energy Source
Context c with hidden state
Context c transforms signal s to s’ at state x c(,s)=s’
Context Recognition is learning c’-1 so that c’-1(s,s’)=
Typical is only nominal and c is no function and c-1 does not exist, so why even try to model it???

## Slide 38: Detection Chain
Feature Extraction & Reduction
Physical Pheno-menon
Activity
Detection
Normalization
Classification
Phenomenon
(e.g. Context Value)
Reasoning
Activity
Physical Pheno-menon
Activity
Detection
Classification
Activity
Ubicomp: Assignments correlated / learned
Classical Measurement methods: Each step analytically modelled

## Slide 39: Unconventional Sensors
Notes: This context awareness and novel form of HCI is based on sensors.
What we used in the Retail Store Application are special types of sensors as the one you see here, that is a extreme high sensitive movement sensor system with almost 0 energy consumption that we develop togehter with Prof. Weber from the IPE (Institut für Prozessdatenverarbeitung und Elektronik) from the Helmholtz Part.
Now we have sensors and we want to build context aware systems out of it. How do we do this?

## Slide 40: Measurement in the 21st century
„A set of observations that reduce uncertainty where the result is expressed as a quantity” Douglas Hubbard: "How to Measure Anything", Wiley (2007)
Result of a measurement: value, mean, other statistical values e.g. standard deviation
  In this sense, a good guess may not be worse than a bad measurement

## Slide 41: Activity Recognition Using RF Signals